## Slide 1
DIGITAL LOGIC DESIGN / PROJECT
SEQUENTIAL LOGIC CIRCUITS
SR Latch • D Flip-Flop • JK Flip-Flop • T Flip-Flop
A Logisim design and simulation project
2620040155 — Laasya Gayathri 2620040156 — Ananya 2620040159 — KVS Karthik 2620040160 — V Pavan Teja
STATE • MEMORY • TIMING

## Slide 2
Introduction: Memory & State
02 • SEQUENTIAL LOGIC
WHAT IS A SEQUENTIAL CIRCUIT?
• Stores binary information (Q = 0 or 1)
• Output depends on inputs and previous state
• Feedback lets a circuit retain its state
PROJECT OBJECTIVES
• Design an SR latch
• Implement D, JK and T flip-flops
• Verify state changes with truth tables and Logisim
INPUTS
Control what happens to stored data.
STATE
Q is the stored bit; Q̅ is its complement.
TIMING
A control level or clock edge determines when state can change.
KEY NOTATION
Q(next) = next output state • ↑ = rising edge • ↓ = falling edge

## Slide 3
SR Latch and D Flip-Flop
03 • SEQUENTIAL LOGIC
SR LATCH — NOR IMPLEMENTATION
Cross-coupled NOR gates feed each output back to the opposite gate.
S sets Q = 1; R resets Q = 0.
S
R
Q(next)
Meaning
0
0
Q
Hold
0
1
0
Reset
1
0
1
Set
1
1
Invalid
Forbidden
NOR SR latch inputs are active-high.
D FLIP-FLOP
At the active clock edge, the flip-flop copies D to Q. Between edges, Q holds its value.
D
Q(next)
0
0
1
1
CHARACTERISTIC EQUATION
Q(next) = D
Use: registers and data storage.

## Slide 4
JK and T Flip-Flops
04 • SEQUENTIAL LOGIC
JK FLIP-FLOP
The JK flip-flop removes the SR latch’s forbidden input case.
J
K
Q(next)
Meaning
0
0
Q
Hold
0
1
0
Reset
1
0
1
Set
1
1
Q̅
Toggle
CHARACTERISTIC EQUATION
Q(next) = JQ̅ + K̅Q
T FLIP-FLOP
T = 0 holds the state. T = 1 toggles Q at the active clock edge.
T
Q
Q(next)
Meaning
0
0
0
Hold
0
1
1
Hold
1
0
1
Toggle
1
1
0
Toggle
CHARACTERISTIC EQUATION
Q(next) = T ⊕ Q

## Slide 5
Timing, Logisim Design & Test Plan
05 • SEQUENTIAL LOGIC
LEVEL-TRIGGERED LATCH
Responds while enable is at its active level. Input changes can affect output during the enabled interval.
EDGE-TRIGGERED FLIP-FLOP
Captures input only at a clock transition (↑ or ↓). Output normally holds between clock edges.
IMPLEMENT IN LOGISIM
• Create a separate circuit for each element
• Build the SR latch with two cross-coupled NOR gates
• Add inputs, clock, Q and Q̅ where available
• Use Poke to change inputs and clock
TEST SEQUENCES
• SR: 00 → 10 → 00 → 01 (hold, set, hold, reset)
• D: test D = 0 then D = 1 at active edge
• JK: 00 → 10 → 01 → 11
• T: 0 → 1 → 1 (toggle on each active edge)

## Slide 6
Applications & Conclusion
06 • SEQUENTIAL LOGIC
APPLICATIONS
• Registers and temporary data storage
• Counters and frequency division
• State machines and control units
• Switch debouncing and timing circuits
KEY TAKEAWAYS
• SR latch stores one bit using feedback
• D stores sampled data
• JK supports hold, set, reset and toggle
• T toggles state when enabled
• Logisim verifies behaviour before hardware implementation
THANK YOU
Questions?